## Slide 1
Chapter 1
Introductory Concepts

## Slide 2
Chapter Outline
1–1 Digital and Analog Quantities
1–2 Binary Digits, Logic Levels, and Digital Wave forms
1–3 Basic Logic Functions
1–4 Combinational and Sequential Logic Functions
1–5 Introduction to Programmable Logic
1–6 Fixed-Function Logic Devices
1–7 Test and Measurement Instruments
1–8 Introduction to Troubleshooting

## Slide 3
Chapter Objectives
Explain the basic differences between digital and analog quantities
Show how voltage levels are used to represent digital quantities
Describe various parameters of a pulse waveform such as rise time, fall time, pulse width, frequency, period, and duty cycle
Explain the basic logic functions of NOT, AND, and OR
Describe several types of logic operations and explain their application in an example system

## Slide 4
Chapter Objectives
Describe programmable logic, discuss the various types, and describe how PLDs are programmed
Identify fixed-function digital integrated circuits according to their complexity and the type of circuit packaging
Identify pin numbers on integrated circuit packages
Recognize various instruments and understand how they are used in measurement and troubleshooting digital circuits and systems
Describe basic troubleshooting methods

## Slide 5
Digital and Analogue Quantities
An analog quantity is one having continuous values.
  Intensity of Light
  Temperature
  Velocity
A digital quantity is one having a discrete set of values
Notes: 5
Most of the quantities in nature that we can measure are continuous, for example the intensity of light, temperature, velocity all change continuously.
Temperature for example never rises in discrete steps like 37, 39, 43. The rise in temperature is continuous.

## Slide 6
Continuous Signal
Notes: 6
The diagram shows a plot of temperature continuously varying with time.
The continuous signal might be representing the change in the intensity of light or velocity.
The continuous signal can be represented digitally by taking samples at regular but fixed intervals.

## Slide 7
Continuous Signal
Notes: 7
In this case 15 samples at regular time intervals are collected.
The 15 samples having the values 1, 2,4,7,18,34,25,23,35,37,29,42,41,25 and 22 represent the continuous signal digitally.
The digital representation of the continuous signal only approximates the original signal and does not truly represent the original signal as can be seen by plotting the digital values.

## Slide 8
Digital Representation
Notes: 8
The reconstructed continuous signal does not give an exact replica of the original.
The reconstructed signal has sharp edges and corners in contrast to the original signal which has smooth curves.

## Slide 9
Under Sampling
Notes: 9
If the number of samples that are collected are reduced by half, that is samples are collected at every odd interval of time, the resulting reconstructed signal is very different from the original signal.
The peak in the continuous signal at 34 0C and the dip at 23 0C are all together missing from the reconstructed signal.
This is due to the small number of samples taken.
A better approximation of the original signal can be obtained by increasing the number of samples.
An infinite number of samples very accurately represent the original continuous signal.

## Slide 10
Merits of Digital Systems
Efficient Processing & Data Storage
Efficient & Reliable Transmission
Detection and Correction of Errors
Precise & Accurate Reproduction
Easy Design and Implementation
Occupy minimum space
Notes: 10
Let us have a quick look at the advantages of a Digital System.
Processing and Storage of digital data is efficient.
  Computers are very efficient at processing information that is in digital binary form.
  A CD can store large number of digitized audio and video clips. Storing same number of audio or video clips in an analogue form requires a large number of audio or video cassettes.
Transmission of digital data is efficient and reliable and less prone to errors.
Even if an error occurs detection and correction of errors in digital data is easier.
  We will be looking at a simple example of detecting errors using the parity bit method.
Digitally stored data can be precisely and accurately reproduced.
  The picture quality and sound quality of digitized video or audio stored on CDs can be reproduced with a far superior quality as compared to analogue audio and video.
Digital circuits and systems are easier to design and implement.
  We would be looking at some simple digital systems in the Digital Logic Design course.
Digital circuits in the form of Integrated circuits occupy very small space.
  The PC has a motherboard which has an area less than 1 sq.ft but has all the important circuitry of the computer.
  Digital memory implemented as an Integrated circuit small enough to fit in you hand can store an entire collection of books!

## Slide 11
Electronic Processing
Analogue Systems
Digital Systems
Representing quantities
in Digital Systems
Notes: 11
Electronic processing of these continuous and digital quantities requires that these quantities be converted into and represented in term of voltages.
Analogue Electronic Systems deal with electronic signals or voltages that are continuous and represent continuous quantities.
Thus a temperature transducer converts a continuous temperature of 39 0C into 39 mVs and 42.75 0C into 42.75 mVs.
Digital Electronic Systems on the other hand deal with discrete electronic signals or voltages that represent discrete or digital values.
How does a digital system such as a calculator process the number 39? Do the Digital systems represent discrete values in terms of voltages? Lets have a look.
One possible solution is to calibrate the electronic circuitry of the calculator to represent the number 1 by 1 mV. The number 10 is represented by 10 mV. The number 39 is represented by 39 mV.

## Slide 12
Representing Digital Values
39 0C ?
39mV
6.25 x 1015 V !!
Digital System
6.25 x 1018 ?
Notes: 12
Consider the Calculator which is an example of a Digital system.
Let us assume that the calculator has been internally calibrated to represent the number 1 by 1mVolts.
Thus a number or temperature value 39 is represented by the calculator in terms of a voltage value as 39 mVolts.
Calculators can also handle a large values such as 6.25 x 1018 the number of electrons in 1 Coulomb of charge.
This large value represented in terms of voltage by the calculator, turns out to be 6.25 x 1015 volts, which is a very large voltage value and can not be practically represented by any circuit.

## Slide 13
Digital Systems
Two Voltage Levels
Two States
  On/Off
  Black/White
  Hot/Cold
  Stationary/Moving
Notes: 13
Digital systems use electronic circuitry that only works with two voltage levels. The two voltage levels represent two states. A voltage level of 5v represents logic high or logic 1 state and a voltage level of 0v represents logic low or logic 0 state.
The two states in a digital system can represent any two quantities, the numbers 0/1, on/off, black/white, hot/cold, moving/stationary and similar other quantities.
How does one represent more than two states in a digital system?
Such as the different shades of grey in between the colours black and white or the temperature 39 or the velocity of a moving object.

## Slide 14
Binary Number System
Binary Numbers
Representing Multiple Values
Combination of 0v & 5v
In digital systems, combinations of the two states, called codes, are used to represent information.
Info Note:
The concept of a digital computer
can be traced back to Charles
Babbage, who developed a crude
mechanical computation device in
the 1830s. John Atanasoff was the
first to apply electronic processing
to digital computing in 1939. In
1946, an electronic digital computer
called ENIAC was implemented
with vacuum-tube circuits. Even
though it took up an entire room,
ENIAC didn’t have the computing
power of your handheld calculator
Notes: 14
The two states of the Digital circuits are based on the Binary number system which allows only two numbers 0 and 1.
The Binary digit is called a bit.
To represent more than two states a combination of binary bits is used.
In the decimal number system a single digit can represent 10 values from 0 to 9.
To represent more than 10 values a combination of two digits is used which allows up to 100 values to be represented.
In a binary number system a combination of 2 bits allows 4 different values to be represented.
For example the four shades are represented by two bits, 00, 01, 10, 11.
A temp of 39 is represented by a combination of six bits 100111.
The number 39 is represented in a digital system by a combination of voltage levels 5, 0, 0, 5, 5 and 5 volts

## Slide 15
Digital Level
The voltages used to represent a 1 and a 0 are called logic levels.
Ideally, one voltage level represents a HIGH and another voltage level represents a LOW.
In a practical digital circuit, however, a HIGH/LOW can be any voltage between a specified minimum value and a specified maximum value.

## Slide 17
Digital Waveforms
Digital waveforms consist of voltage levels that are changing back and forth between the HIGH and LOW levels or states.
A digital waveform is made up of a series of pulses.
a pulse has two edges: a leading edge that occurs first at time t0 and a trailing edge that occurs last at time t1.
Notes: a pulse has two edges: a leading edge that occurs first at time t0
and a trailing edge that occurs last at time t1.
17

## Slide 18
Information Processing
Numbers
Text
Formula and Equations
Drawings and Pictures
Sound and Music
Notes: 18
A computer which is a digital system can process different types of information
It can handle numbers and perform arithmetic operations on the numbers
It can handle text and perform editing operations on text
It can handle mathematical and scientific formulas
It can handle drawings and pictures
It can process sound and music
All this diverse types of information is represented in the form of binary numbers. Different binary standards are used to represent different types of information. For example, text is represented through binary bits, however the bits representing the characters follow a standard ASCII code

## Slide 19
Logic
logic is the realm of human reasoning that tells you a certain proposition (declarative statement) is true if certain conditions are true
“The light is on” will be true if “The bulb is not burned out” is true and if “The switch is on” is true. Therefore, this logical statement can be made: The light is on only if the bulb is not burned out and the switch is on.
Several propositions, when combined, form propositional, or logic, functions.
The term logic is applied to digital circuits used to implement logic functions.

## Slide 20
Logic Gates
Building Blocks
AND, OR and NOT Gates
NAND, NOR, XOR and XNOR Gates
Integrated Circuits (ICs)
Notes: 20
How does the digital circuit process the binary information?
As mentioned earlier, the digital circuits are designed to work with binary numbers.
Logic Gates which are the Basic building blocks of a complex digital system which perform simple but unique operations on the binary or digital information.
The basic Logic Gates are the AND Gate, OR Gate and the NOT Gate.
Each of these three gates performs unique logical operations on the information applied at the outputs. The result of the operation is available on the output of the gate.
Other gates that are also frequently used are NAND, NOR, XOR and XNOR. The four gates are symbolically represented in the diagram.
All these gates are available in the form of Integrated Circuits (ICs)

## Slide 21
Logic Gate Symbol and ICs
1
2
3
4
5
6
G
N
D
V
c
c
1
3
1
2
1
1
1
0
9
8
7400
inverter.
Notes: 21
Each gate is shown to have two inputs except for the NOT gate.
The six gates can have more than two inputs.
All logic gates always have a single output.
The Integrated Circuit shows a NAND Gate IC which has four dual input NAND gates.
Such ICs with different gates are available and used for implementing digital circuits.

## Slide 22
Combinational Circuits
Combination of Logic Gates
Adder Combinational Circuit
Notes: 22
The Logic gates by them selves are not able to do anything useful. These gates have to be connected together to form a circuit which is able to perform some useful function. A circuit formed by the combination of logic gates is known as a combinational circuit.
An Adder combination circuit is shown in the diagram.

## Slide 23
Adder Combinational Circuit
Notes: 23
An Adder circuit is formed by the combination of AND, OR and XOR gates and is able to add two single bit binary numbers.
Combinational circuits perform an operation on the input binary information and results in an output which is almost instantaneous.
Many of these combinational circuits that perform a specific function such as addition are available as MSI Integrated Circuits (ICs) and are known as functional devices.
Other commonly used Functional devices are

## Slide 24
Sum
Carry

## Slide 25
Functional Devices
Functional Devices
  Adders
  Comparators
  Encoders/Decoders
  Multiplexers/Demultiplexers
Notes: 25
Commonly used functional ICs are
  Adder
  Comparator
  Encoder/Decoder
  Multiplexer/Demultiplexer

## Slide 26
Sequential Circuits
Memory Element
Current & Previous State
Flip-Flops
Counters & Registers
Notes: 26
Digital systems are being used in a wide variety of applications. A large number of these digital systems generate an output based on not only the current information but some previously stored information.
Consider a timer circuit, counting in reverse from 10 to 0. The timer circuit decrements the count by 1 each time it receives an input signal. The new count value is dependent on the previous count value.
Consider the block diagram of a Sequential circuit.
The Sequential circuit consists of a Combinational part and a memory element.
Consider the timer of a microwave oven. You key in the time to cook your favourite dish.
The microwave display unit displays the cooking time.
The memory element of the microwave oven sequential circuit stores the cooking time.
The cooking time is decremented by 1 after every second when a new input signal is received at the input of the combinational part of the Sequential circuit.
Ultimately, when the cooking time decrements to zero and the memory element stores zero , the next input signal sounds an alarm and turns the microwave off.
A traffic signal controller operates in a similar manner. It switches between the green, amber and red signal in a sequence on the basis of current and previous information.
The memory or storage element in the Sequential Circuit is implemented using a very simple digital circuit known as a flip-flop.
Examples of Sequential circuits are Counters and Registers. These Sequential circuits are available as MSI ICs.

## Slide 27
Programmable Logic Devices (PLDs)
Configurable Hardware
Combinational Circuits
Sequential Circuits
Low chip count
Lower Cost
Short development time
Notes: 27
A modern trend in implementing digital systems is through Programmable Logic Devices or PLDs.
PLDs provide the user with a general purpose circuitry which the user can configure or program to form any combinational or Sequential functional unit.
The adder circuit discussed earlier is a combinational circuit that uses AND, OR and XOR Gates. Thus three different ICs have to be used to implement an adder.
A PLD based implementation only requires a single chip.
The use of PLDs in implementing combinational and sequential circuits results in fewer ICs and thus lower costs. The implementation time is also short.

## Slide 28
Memory
Storage
RAM (Random Access Memory)
  Read-Write
  Volatile
ROM (Read-Only Memory)
  Read-Only
  Non-Volatile
Notes: 28
Memory is an important requirement of a digital system. Besides its use to implement sequential circuits, large memory is required to store information in computer systems. Essentially memory is of two types.
RAM (Random Access Memory) which also stored information to be read or modified.
RAMs are volatile, that is if the power is turned off, the contents stored in the memory are lost.
ROM (Read-Only Memory) as the name specifies allows only read operations. No new information is allowed to be written into the memory.
ROMs are non-volatile and retain the information even if the power is turned off.

## Slide 29
A/D & D/A Converters
Processing of Continuous values
Conversion
  Analogue to Digital A/D
  Digital to Analogue D/A
Industrial Control Application
Notes: 29
Real-world quantities as mention earlier are continuous in nature and have widely varying ranges. Processing of real-world information can be efficiently and reliably done in the digital domain.
This requires real-world quantities to be read and converted into equivalent digital values which can be processed by a digital system. In most cases the processed output needs to be converted back into real-world quantities.
Two conversions are required, one from the real-world to the digital domain and then back from the digital domain to the real-world.
Modern digitally controlled industrial units extensively use Analogue to Digital (A/D) and Digital to Analogue (D/A) converters to covert quantities represented as an analogue voltage into an equivalent digital representation and vice versa.
The diagram shows a chemical reaction vessel being heated to expedite the chemical reaction.

## Slide 30
A Process Control System
Notes: 30
A system for bottling vitamin tablets is shown in the block diagram of Figure 1–28. This
example system shows how the various logic functions that have been introduced can be
used together to form a total system. To begin, the tablets are fed into a large funnel-type
hopper. The narrow neck of the hopper creates a serial flow of tablets into a bottle on
the conveyor belt below. Only one tablet at a time passes the sensor, so the tablets can
be counted. The system controls the number of tablets into each bottle and displays a
continually updated readout of the total number of tablets bottled.
General Operation
The maximum number of tablets per bottle is entered from the keypad, changed to a code
by the Encoder, and stored in Register A. Decoder A changes the code stored in the register
to a form appropriate for turning on the display. Code converter A changes the code to a
binary number and applies it to the A input of the Comparator (Comp).
An optical sensor in the neck of the hopper detects each tablet that passes and produces
a pulse. This pulse goes to the Counter and advances it by one count; thus, any time during
the filling of a bottle, the binary state of the counter represents the number of tablets in the
bottle. The binary count is transferred from the counter to the B input of the comparator
(Comp). The A input of the comparator is the binary number for the maximum tablets per
bottle. Now, let’s say that the present number of tablets per bottle is 50. When the binary
number in the counter reaches 50, the A = B output of the comparator goes HIGH, indicating
that the bottle is full.
The HIGH output of the comparator causes the valve in the neck of the hopper to close and
stop the flow of tablets. At the same time, the HIGH output of the comparator activates the
conveyor, which moves the next empty bottle into place under the hopper. When the bottle is in
place, the conveyor control issues a pulse that resets the counter to zero. As a result, the output
of the comparator goes back LOW and causes the hopper valve to restart the flow of tablets.
For each bottle filled, the maximum binary number in the counter is transferred to the
A input of the Adder. The B input of the adder comes from Register B that stores the total
number of tablets bottled up through the last bottle filled. The adder produces a new cumulative
sum that is then stored in register B, replacing the previous sum. This keeps a running
total of the tablets bottled during a given run.
The cumulative sum stored in register B goes to Decoder B, which detects when Register
B has reached its maximum capacity and enables the MUX, which converts the binary
from parallel to serial form for transmission to the remote DEMUX. The DEMUX converts
the data back to parallel form for storage.

## Slide 31
Summary
Continuous Signals
Digital Representation in Binary
Information Processing
Logic Gates
Notes: 31
We have discussed that many of the measurable quantities in nature are continuous
For efficient processing these continuous signals are digitized and represented as binary voltage values
Digital systems are able to process different types of information such as numbers, text, drawings, pictures and sound.
All this different type of information is represented digitally in terms of binary numbers.
Logic Gates are the basic building blocks of all digital circuits and these gates are able to perform simple logical operations on binary information.

## Slide 32
Summary
Combinational & Sequential Circuits
Programmable Logic Devices (PLDs)
Memory (RAM & ROM)
A/D & D/A Converters
Notes: 32
Practical digital circuits are formed by combining various logic gates. Such circuits are known as combinational circuits.
Sequential circuits are a combination of combinational circuits with a storage element.
PLDs are available as general purpose configurable Integrated Circuit.
Users can program a PLD to implement any combinational or sequential circuit.
Memory is an essential part of any digital system.
Memory is used to store information.
Two types of memory, RAM and ROM are used.
Finally, we looked at A/D and D/A converters.
A/D and D/A converters allow conversion of analogue values to digital values and vice versa.
These converters allow digital systems to process and control real world quantities.