## Slide 1: Digital Fundamentals
CHAPTER 4 Boolean Algebra and Logic Simplification

## Slide 2: Chapter Outline
4–1 Boolean Operations and Expressions
4–2 Laws and Rules of Boolean Algebra
4–3 DeMorgan’s Theorems
4–4 Boolean Analysis of Logic Circuits
4–5 Logic Simplification Using Boolean Algebra
4–6 Standard Forms of Boolean Expressions
4–7 Boolean Expressions and Truth Tables
4–8 The Karnaugh Map
4–9 Karnaugh Map SOP Minimization
4–10 Karnaugh Map POS Minimization
4–11 The Quine-McCluskey Method
4–12 Boolean Expressions with VHDL Applied Logic

## Slide 3: Boolean Operations and Expressions

## Slide 4: Boolean Operations and Expressions
Addition
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = 1
Multiplication
  0 * 0 = 0
  0 * 1 = 0
  1 * 0 = 0
  1 * 1 = 1

## Slide 5: Checkup
1. If A = 0, what does A equal?
2. Determine the values of A, B, and C that make the sum term A + B + C equal to 0.
3. Determine the values of A, B, and C that make the product term ABC equal to 1.

## Slide 6: Laws and Rules of Boolean Algebra

## Slide 7: Laws Boolean Algebra
Commutative Laws
Associative Laws
Distributive Law

## Slide 8: Laws of Boolean Algebra
Commutative Law of Addition:
A + B = B + A

## Slide 9: Laws of Boolean Algebra
Commutative Law of Multiplication:
A * B = B * A

## Slide 10: Laws of Boolean Algebra
Associative Law of Addition:
A + (B + C) = (A + B) + C

## Slide 11: Laws of Boolean Algebra
Associative Law of Multiplication:
A * (B * C) = (A * B) * C

## Slide 12: Laws of Boolean Algebra
Distributive Law:
A(B + C) = AB + AC

## Slide 13: Checkup
Apply the associative law of addition to the expression
A + (B + C + D).
2. Apply the distributive law to the expression
A(B + C + D).
Solution:
A + (B + C + D) = (A + B + C )+ D
A(B + C + D) = AB + AC + AD)

## Slide 14: Rules of Boolean Algebra

## Slide 15: Rules of Boolean Algebra
Rule 1
OR Truth Table

## Slide 16: Rules of Boolean Algebra
Rule 2
OR Truth Table

## Slide 17: Rules of Boolean Algebra
Rule 3
AND Truth Table

## Slide 18: Rules of Boolean Algebra
Rule 4
AND Truth Table

## Slide 19: Rules of Boolean Algebra
Rule 5
OR Truth Table

## Slide 20: Rules of Boolean Algebra
Rule 6
OR Truth Table

## Slide 21: Rules of Boolean Algebra
Rule 7
AND Truth Table

## Slide 22: Rules of Boolean Algebra
Rule 8
AND Truth Table

## Slide 23: Rules of Boolean Algebra
Rule 9

## Slide 24: Rules of Boolean Algebra
Rule 10: A + AB = A
AND Truth Table
OR Truth Table

## Slide 25: Rules of Boolean Algebra
Rule 11:
AND Truth Table
OR Truth Table

## Slide 26: Rules of Boolean Algebra
Rule 12: (A + B)(A + C) = A + BC
AND Truth Table
OR Truth Table

## Slide 27: 4–3 DeMorgan’s Theorem
State DeMorgan’s theorems
Relate DeMorgan’s theorems to the equivalency of the
  NAND and negative-OR gates
  NOR and negative-AND gates
Apply DeMorgan’s theorems to the simplification of Boolean expressions
Notes: In Chapter 3 we have discussed (Slide # 31)
NAND and negative-OR gates
NOR and negative-AND gates
DeMorgan’s theorems provide mathematical verification of the equivalency of the NAND and negative-OR gates and the equivalency of the NOR and negative-AND gates,
After completing this section, you should be able to

## Slide 28: DeMorgan’s Theorems
Theorem 1
Theorem 2
Remember:
  “Break the bar, change the sign”
Notes: DeMorgan’s first theorem is stated as follows:
The complement of a product of variables is equal to the sum of the complements of the variables.
Stated another way,
The complement of two or more ANDed variables is equivalent to the OR of the complements of the individual variables.
DeMorgan’s second theorem is stated as follows:
The complement of a sum of variables is equal to the product of the complements of the variables.
Stated another way,
The complement of two or more ORed variables is equivalent to the AND of the complements of the individual variables.

## Slide 32: Applying DeMorgan’s Theorems

## Slide 33: Applying DeMorgan’s Theorems

## Slide 34: Applying DeMorgan’s Theorems

## Slide 35: Applying DeMorgan’s Theorems

## Slide 36: Applying DeMorgan’s Theorems

## Slide 37: Applying DeMorgan’s Theorems

## Slide 41: Checkup

## Slide 42: 4–4 Boolean Analysis of Logic Circuits
Determine the Boolean expression for a combination of gates
Evaluate the logic operation of a circuit from the Boolean expression
Construct a truth table
Notes: Boolean algebra provides a concise way to express the operation of a logic circuit formed by a combination of logic gates so that the output can be determined for various combinations of input values. After completing this section, you should be able to

## Slide 43: Figure 4–16 A logic circuit showing the development of the Boolean expression for the output.
CD
B + CD
A(B + CD)

## Slide 44: Evaluating the Expression
A(B + CD), first find the values of the variables that make the
expression equal to 1, using the rules for Boolean addition and multiplication. In this case, the expression equals 1 only if A = 1 and B + CD = 1 because
A(B + CD) = 1.1 = 1
Now determine when the B + CD term equals 1.
The term B + CD = 1 if either B = 1 or CD = 1 or if both B and CD equal 1 because
B + CD = 1 + 0 = 1
B + CD = 0 + 1 = 1
B + CD = 1 + 1 = 1
The term CD = 1 only if C = 1 and D = 1.
summarize, the expression A(B + CD) = 1 when A = 1 and B = 1 regardless of
the values of C and D or when A = 1 and C = 1 and D = 1 regardless of the value of B.
The expression A(B + CD) = 0 for all other value combinations of the variables

## Slide 45: Putting the Results in Truth Table Format
The first step is to list the sixteen input variable combinations of 1s and 0s in a binary sequence as shown in Table 4–5.
Next, place a 1 in the output column for each combination of input variables that was determined in the evaluation.
Finally, place a 0 in the output column for
all other combinations of input variables.

## Slide 46: Checkup
1. Replace the AND gates with OR gates and the OR gate with an AND gate in Figure 4–18. Determine the Boolean expression for the output.
2. Construct a truth table for the circuit in Question 1.
Solution:
(C + D)B + A
The expression is a 1 when A is 1 or when B and C are 1s or when B
and D are 1s. The expression is 0 for all other variable combinations.

## Slide 47: 4–5 Logic Simplification Using Boolean Algebra
A simplified Boolean expression uses the fewest gates possible to implement a given
expression.
Using Boolean algebra techniques, simplify this expression:
AB + A(B + C) + B(B + C)
Solution
The following is not necessarily the only approach.
Step 1: Apply the distributive law to the second and third terms in the expression, as follows:
AB + AB + AC + BB + BC
Step 2: Apply rule 7 (BB = B) to the fourth term.
AB + AB + AC + B + BC
Step 3: Apply rule 5 (AB + AB = AB) to the first two terms.
AB + AC + B + BC
Step 4: Apply rule 10 (B + BC = B) to the last two terms.
AB + AC + B
Step 5: Apply rule 10 (AB + B = B) to the first and third terms.
B + AC

## Slide 48: 4–5 Logic Simplification Using Boolean Algebra

## Slide 49: 4–5 Logic Simplification Using Boolean Algebra

## Slide 50: 4-6 Standard Forms of Boolean Expressions
Identify a sum-of-products expression
Determine the domain of a Boolean expression
Convert any sum-of-products expression to a standard form
Evaluate a standard sum-of-products expression in terms of binary values
Identify a product-of-sums expression
Convert any product-of-sums expression to a standard form
Evaluate a standard product-of-sums expression in terms of binary values
Convert from one standard form to the other

## Slide 51: Standard Forms of Boolean Expressions
The sum-of-product (SOP) form
    Example: X = AB + CD + EF
The product of sum (POS) form
    Example: X = (A + B)(C + D)(E + F)
Notes: All Boolean expressions, regardless of their form, can be converted into either of two standard forms: the sum-of-products form or the product-of-sums form
Standardization makes the evaluation, simplification, and implementation of Boolean expressions much more systematic
and easier.

## Slide 52: The Sum-of-Products (SOP) Form
A product term: a term consisting of the product (Boolean multiplication) of literals (variables or their complements).
When two or more product terms are summed by Boolean addition, the resulting expression is a sum-of-products(SOP).

## Slide 53: Domain of a Boolean Expression
The domain of a general Boolean expression is the set of variables contained in the expression in either complemented or un-complemented form. For example,
AB + ABC is the set of variables A, B, C
ABC + CDE + BCD is the set of variables A, B, C, D, E.

## Slide 54: Figure 4–18 Implementation of the SOP expression AB + BCD + AC.

## Slide 55: Figure 4–19 This NAND/NAND implementation is equivalent to the AND/OR in Figure 4–18.

## Slide 56: Figure 4–19 This NAND/NAND implementation is equivalent to the AND/OR in Figure 4–18.

## Slide 57: Conversion of a General Expression to SOP Form
Any logic expression can be changed into SOP form by applying Boolean algebra techniques.
For example,
A(B + CD)
=> AB + ACD //distributive law:

## Slide 58: The Karnaugh Map

## Slide 59: The Karnaugh Map
3-Variable Karnaugh Map
3-Variable Example

## Slide 60: The Karnaugh Map
4-Variable Karnaugh Map
4-Variable Example

## Slide 61: Figure 4–23 Adjacent cells on a Karnaugh map are those that differ by only one variable. Arrows point between adjacent cells.

## Slide 62: Figure 4–24 Example of mapping a standard SOP expression.

## Slide 63: Figure 4–25

## Slide 64: Figure 4–28

## Slide 65: Figure 4–29

## Slide 66: Figure 4–30

## Slide 67: Figure 4–31

## Slide 68: Figure 4–32

## Slide 69: Figure 4–33

## Slide 70: Figure 4–34

## Slide 71: Figure 4–35 Example of mapping directly from a truth table to a Karnaugh map.

## Slide 72: Figure 4–36 Example of the use of “don’t care” conditions to simplify an expression.

## Slide 73: Figure 4–37 Example of mapping a standard POS expression.

## Slide 74: Figure 4–38

## Slide 75: Figure 4–39

## Slide 76: Figure 4–40

## Slide 77: Figure 4–41

## Slide 78: The Karnaugh Map
5-Variable Karnaugh Mapping

## Slide 79: Figure 4–43 Illustration of groupings of 1s in adjacent cells of a 5-variable map.

## Slide 80: Figure 4–44

## Slide 81: VHDL

## Slide 82: Figure 4–45 A VHDL program for a 2-input AND gate.

## Slide 83: VHDL
VHDL Operators
    and
    or
    not
    nand
    nor
    xor
    xnor
VHDL Elements
  entity
  architecture

## Slide 84: VHDL
Entity Structure
  Example:
      entity AND_Gate1 is
        port(A,B:in bit:X:out bit);
      end entity AND_Gate1

## Slide 85: VHDL
Architecture
  Example:
    architecture LogicFunction of AND_Gate1 is
    begin
      X<=A and B;
    end architecture LogicFunction

## Slide 86: Figure 4–46

## Slide 87: Hardware Description Languages (HDL)
Boolean Expressions in VHDL
    AND X <= A and B;
    OR X <= A or B;
    NOT X <= A not B;
    NAND X <= A nand B;
    NOR X <= A nor B;
    XOR X <= A xor B;
    XNOR X <= A xnor B;

## Slide 88: Figure 4–47 Seven-segment display format showing arrangement of segments.

## Slide 89: Figure 4–48 Display of decimal digits with a 7-segment device.

## Slide 90: Figure 4–49 Arrangements of 7-segment LED displays.

## Slide 91: Figure 4–50 Block diagram of 7-segment logic and display.

## Slide 92: Figure 4–51 Karnaugh map minimization of the segment-a logic expression.

## Slide 93: Figure 4–52 The minimum logic implementation for segment a of the 7-segment display.

## Slide 94: Summary

## Slide 95: Figure 4–54

## Slide 96: Figure 4–55. What is the Boolean expression for each of the logic gates?

## Slide 97
Figure 4–56. What is the Boolean expression for each of the logic gates?

## Slide 98: Figure 4–58. Derive a standard SOP and standard POS expression for each truth table.

## Slide 99: Figure 4–59. Reduce the function in the truth table to its minimum SOP form by using a Karnaugh map.

## Slide 100: Figure 4–62. Example 4-21. Related Problem answer.

## Slide 101: Figure 4–63. Example 4-22. Related Problem answer.

## Slide 102: Figure 4–64. Example 4-23. Related Problem answer.

## Slide 103: Figure 4–65. Example 4-24. Related Problem answer.

## Slide 104: Figure 4–66. Example 4-30. Related Problem answer.