## Slide 1: Digital Fundamentals
CHAPTER 6 Functions of Combinational Logic

## Slide 2: Chapter Outline
6–1 Half and Full Adders
6–2 Parallel Binary Adders
6–3 Ripple Carry and Look-Ahead Carry Adders
6–4 Comparators
6–5 Decoders
6–6 Encoders
6–7 Code Converters
6–8 Multiplexers (Data Selectors)
6–9 Demultiplexers
6–10 Parity Generators/Checkers
6–11Troubleshooting Applied Logic

## Slide 3: Basic Adders
Half-Adder - The half-adder accepts two binary digits on its inputs and produces two binary digits on its outputs.
Sum bit and Carry bit are outputs.
Full-Adder - Full-adder accepts two input bits and an input carry bit and generates a sum output and an output carry bit.

## Slide 4: Half-Adder
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
Zero plus zero equals zero
Zero plus one equals one
One plus zero equals one
One plus one equals zero with a carry of one
Simple Binary Addition

## Slide 5: Half-Adder

## Slide 6: Full-Adder – Extra Input

## Slide 7: Figure 6–4 Full-adder logic.

## Slide 8: Full-Adder
Full adder from two half-adder circuits

## Slide 9: Figure 6–6. Determine the outputs for the inputs shown.
Inputs are A = 1, B = 0, and Cin = 0.
Outputs are
Σ = 1 and Cout = 0.
Inputs are A = 1, B = 1, and Cin = 0.
Outputs are Σ = 0 and Cout = 1.
Inputs are A = 1, B = 0, and Cin = 1.
Outputs are Σ = 0 and Cout = 1.

## Slide 11: Parallel Binary Adders
To add binary numbers with more than one bit, you must use additional full-adders.
1
1 1
+ 0 1 1 0 0
Carry bit from right column
Carry bit from second column becomes a sum bit.
Two or more full-adders are connected to form parallel binary adders.

## Slide 12: Parallel Binary Adders
Two-bit parallel binary adder using two full-adders.

## Slide 13: Parallel Binary Adders
Find the sum generated by the 3-bit parallel adder. Show the intermediate carries when the binary numbers 101 (A) and 011 (B) are added.
4
1
0
0
1
1
1
1
0
0
1
1
0

## Slide 14: Parallel Binary Adders
Four-bit parallel binary adder
Group of four bits is called a nibble. Two nibbles is one byte.

## Slide 15
Use 4-bit parallel adder truth table to find the sum and output carry for the addition of the following two 4-bit numbers. The input carry (Cn-1) is 0.
    A4A3A2A1 = 1100 and B4B3B2B1 = 1100
Cn-1
Cn
For n = 1: A1 = 0, B1 = 0, and Cn-1 = 0.
From 1st row of table: Σ1 = 0 and C1 = 0.
For n = 2: A2 = 0, B2 = 0, and Cn-1 = 0.
From 1st row of table: Σ2 = 0 and C2 = 0.
For n = 3: A3 = 1, B3 = 1, and Cn-1 = 0.
From 4th row of table: Σ3 = 0 and C3 = 1.
For n = 4: A4 = 1, B4 = 1, and Cn-1 = 1.
From last row of table: Σ4 = 1 and C4 = 1.
Result is 11000.
EXAMPLE 6–3

## Slide 16: Figure 6–10 Four-bit parallel adder.
Implementation: 4-Bit Parallel Adder

## Slide 17: Figure 6–12 Examples of adder expansion.
Adders can be expanded to handle more bits by cascading.

## Slide 18: Figure 6–13 Two 74LS283 adders connected as an 8-bit parallel adder (pin numbers are in parentheses).
The following two 8-bit numbers are added. A8A7A6A5A4A3A2A1 = 10111001 and B8B7B6B5B4B3B2B1 = 10011110

## Slide 19: Figure 6–14 A voting system using full-adders and parallel binary adders.

## Slide 21: Figure 6–15 A 4-bit parallel ripple carry adder showing “worst-case” carry propagation delays.

## Slide 22
Ripple Carry Adder suffers from propagation delay
Look-Ahead Carry Adder
  Tries to anticipate the output carry of each stage
  Carry Generation occurs when both inputs are 1
    Cg = AB
  Carry Propagation occurs when input is rippled to the output carry
    Cp = A + B
  Output Carry is a 1 if Cg = 1 or (Cp = 1 AND Cin = 1)
    Cout = Cg + CpCin

## Slide 23: Figure 6–16 Illustration of conditions for carry generation, Cg, and carry propagation, Cp.
Look-Ahead Carry Adder eliminates ripple carry delay. Cout = Cg + CpCin
Cg = A B = 1
Cg = A B = 1
(A + B ) Cin = 1
(A + B ) Cin = 1
(A + B ) Cin = 1

## Slide 24: Figure 6–17 Carry generation and carry propagation in terms of the input bits to a 4-bit adder.
Thomas L. Floyd Digital Fundamentals, 9e
Copyright ©2006 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 25: Figure 6–17 Carry generation and carry propagation in terms of the input bits to a 4-bit adder.
Thomas L. Floyd Digital Fundamentals, 9e
Copyright ©2006 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 26: Figure 6–18 Logic diagram for a 4-stage look-ahead carry adder.
Thomas L. Floyd Digital Fundamentals, 9e
Copyright ©2006 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Notice that Cin is only dependent on inputs, so doesn’t suffer from propagation delay like the ripple adder.

## Slide 27: Comparators
The basic function of a comparator is to compare the magnitudes of two binary quantities
In its simplest form, a comparator circuit determines whether two numbers are equal.

## Slide 28: Comparators
1-Bit Comparator
2-Bit Comparator
4-Bit Comparator

## Slide 29: Comparators
1-Bit Comparator - Exclusive NOR
The output is 1 when the inputs are equal

## Slide 30: Comparators
2-Bit Comparator
The output is 1 when A0 = B0 AND A1 = B1

## Slide 31: Example 6-5: Comparators
Apply each of the following sets of binary numbers to the comparator inputs in Figure 6–20, and determine the output by following the logic levels through the circuit.
(a) 10 and 10 (b) 11 and 10

## Slide 32: Inequality: Comparators
4-Bit Comparator
One of three outputs will be HIGH:
    A greater than B (A > B)
    A equal to B (A = B)
    A less than B (A < B)
To determine an inequality of binary numbers A and B, you first examine the highest-
order bit in each number. The following conditions are possible:
1. If A3 = 1 and B 3 = 0, number A is greater than number B.
2. If A3 = 0 and B 3 = 1, number A is less than number B.
3. If A3 = B 3 , then you must examine the next lower bit position for an inequality.

## Slide 33: Figure 6–23 What are the outputs for the given inputs?
A B 0110 > 0011 YES 0110 = 0011 NO 0110 < 0011 NO
1
0
0

## Slide 34: Figure 6–25 An 8-bit magnitude comparator using two 74HC85s.
Lowest-order comparator must have a LOW on A > B and A < B input and a HIGH on A = B input.

## Slide 35: Decoders
Binary decoder
4-bit decoder
BCD-to-decimal decoder
BCD-to-7-segement decoder

## Slide 36: Decoders
Suppose we want to know when a binary 1001 occurs on the inputs of a digital circuit.
We can use a Decoder for this function.
Binary decoder
  The output is 1 only when:
    A0 = 1
    A2 = 0
    A3 = 0
    A4 = 1
This is only one of an infinite number of examples

## Slide 37
Determine the logic required to decode the binary number 1011 by producing a HIGH level on the output. LSB = A0 (right most)
A0 = 1, A1 = 1, A2 = 0, A3 = 1
X = A3A2A1A0

## Slide 38: Decoders
4-bit decoder (4 line to 16 line decoder or 1 of 16 decoder)
Logic Diagram

## Slide 39: Decoders
4-bit decoder
  Binary inputs
  Active-low outputs (bubbles)
Truth Table
A3A2A1A0 Output 0 1 1 0 6 is low, all other outputs are high

## Slide 40: Decoders
BCD-to-decimal decoder
If 0011 is input, then output 3 is low and all other outputs are high Active Low output since bubbles on outputs.

## Slide 41: Decoders
BCD-to-7-segement decoder
Logic Diagram
Common-anode
Common Anode has all anodes of LEDs tied to +V

## Slide 42: Decoders
BCD-to-7-segment decoder
Truth Table

## Slide 43: Figure 6–35 Pin diagram and logic symbol for the 74LS47 BCD-to-7-segment decoder/driver.
Copyright ©2006 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
LT = Lamp Test - when LOW and BI/RBO is HI then all LEDs are ON BI = Blanking Input RBI = Ripple Blanking Input RBO = Ripple Blanking Output

## Slide 44: Figure 6–36 Examples of zero suppression using the 74LS47 BCD to 7-segment decoder/driver.
Tie RBI of Right to next left BI/RBO for leading zero suppression. Left most RBI is tied to ground.
Tie RBI of Left to next right BI/RBO for trailing zero suppression. Right most RBI is tied to ground.

## Slide 45: Encoders
Decimal-to-BCD encoder
8-line-to-3-line encoder

## Slide 46: Encoders
Decimal-to-BCD encoder ( 10 inputs, 4 outputs)

## Slide 47: Logic Diagram of Decimal-to-BCD Encoder
A3 = 8 + 9
A2 = 4 + 5 + 6 + 7
A1 = 2 + 3 + 6 + 7
A0 = 1 + 3 + 5 + 7 + 9
All odds

## Slide 48: Encoders
8-line-to-3-line encoder
If line 5 on input is high, then output will be 101. Assume only one input is high.

## Slide 49: Code Converters
BCD-to-binary conversion
Binary-Gray conversions

## Slide 50: BCD
Convert BCD number 00100111 to binary.
Could convert to decimal 27 and then convert to binary.
Can add weights.
80 40 20 10 8 4 2 1 0 0 1 0 0 1 1 1 1 1 10 2 100 4
10100 20
0011011 27

## Slide 51: Figure 6–43 Four-bit binary-to-Gray conversion logic.
Convert 1 1 0 0 to Gray
1
0
1
0
XOR

## Slide 52: Figure 6–44 Four-bit Gray-to-binary conversion logic.
Convert 1 0 1 0 to Gray
1
XOR
1
0
0

## Slide 53: Multiplexers (Data Selectors)
4-input multiplexer
Expanded multiplexers

## Slide 54: Multiplexers (Data Selectors)
4-input multiplexer
If Data-Select Inputs are 10, then Y = D2 If D2 = 0, then Y = 0. If D2 = 1, then Y = 1.

## Slide 55
What is the output Y if we have the following inputs?
0 1
1 0 1 0
1
1 1
1 0 1 0
0

## Slide 56: Demultiplexers
Reverses the multiplexing function.
Sends the data input to the selected output.
Decoders can be demultiplexers.

## Slide 57: Demultiplexers
2-line-to-4-line demux

## Slide 58
Find the data-output waveforms for the demultiplexer.
S0 and S1 select which output line will receive the input data.
If data input is zero, then all outputs will be zero.

## Slide 59: Parity Generators/Checkers
Parity generator/checker
Sum of even number of 1s is always 0. Sum of odd number of 1s is always 1.

## Slide 60: Figure 6–76. Problem 4. Find the sum based on the inputs. Note: We are adding A = 111 to B = 101.
0
0
1
1

## Slide 61: Figure 6–80 Problem 14. Plot the 3 outputs (A>B, A=B, A<B)
A3A2A1A0 B3B2B1B0 A>B A = B A<B 1 0 0 1 0 1 0 0 1 0 0 1 1 1 1 1 1 1 1 0 1 0 1 1 1 0 0 0 1 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 1 0 1 1 1 0 0 0 0 1
A>B
A=B
A<B

## Slide 62: Figure 6–84. Problem 22. Find sequence of digits that appear.
A3A2A1A0 0 0 0 0 0 1 0 0 1 9 1 1 1 1 undefined 0 1 1 1 7
3
2
1
0

## Slide 63: Figure 6–85. Like Problem 28.
If S0S1 = 11 and D3D2D1D0 = 1001, what is the output?
= 1