## Slide 1: Digital Fundamentals
CHAPTER 6 Functions of Combinational Logic

## Slide 2: Chapter Outline
6–1 Half and Full Adders
6–2 Parallel Binary Adders
6–3 Ripple Carry and Look-Ahead Carry Adders
6–4 Comparators
6–5 Decoders
6–6 Encoders
6–7 Code Converters
6–8 Multiplexers (Data Selectors)
6–9 Demultiplexers
6–10 Parity Generators/Checkers
6–11Troubleshooting Applied Logic

## Slide 3: Comparators
The basic function of a comparator is to compare the magnitudes of two binary quantities
In its simplest form, a comparator circuit determines whether two numbers are equal.

## Slide 4: Comparators
1-Bit Comparator
2-Bit Comparator
4-Bit Comparator

## Slide 5: Comparators
1-Bit Comparator - Exclusive NOR
The output is 1 when the inputs are equal

## Slide 6: Comparators
2-Bit Comparator
The output is 1 when A0 = B0 AND A1 = B1

## Slide 7: Example 6-5: Comparators
Apply each of the following sets of binary numbers to the comparator inputs in Figure 6–20, and determine the output by following the logic levels through the circuit.
(a) 10 and 10 (b) 11 and 10

## Slide 8: Inequality: Comparators
4-Bit Comparator
One of three outputs will be HIGH:
    A greater than B (A > B)
    A equal to B (A = B)
    A less than B (A < B)
To determine an inequality of binary numbers A and B, you first examine the highest-
order bit in each number. The following conditions are possible:
1. If A3 = 1 and B 3 = 0, number A is greater than number B.
2. If A3 = 0 and B 3 = 1, number A is less than number B.
3. If A3 = B 3 , then you must examine the next lower bit position for an inequality.

## Slide 9: Inequality: Comparators
1-Bit Comparator
One of three outputs will be HIGH:
    A greater than B (A > B)
    A equal to B (A = B)
    A less than B (A < B)

## Slide 10: Inequality: Comparators
1-Bit Comparator
One of three outputs will be HIGH:
    A greater than B (A > B)
    A equal to B (A = B)
    A less than B (A < B)

## Slide 11: Inequality: Comparators
2-Bit Comparator

## Slide 12: Inequality: Comparators
2-Bit Comparator

## Slide 13: Inequality: Comparators
2-Bit Comparator

## Slide 14: Inequality: Comparators
2-Bit Comparator

## Slide 15: Figure 6–23 What are the outputs for the given inputs?
A B 0110 > 0011 YES 0110 = 0011 NO 0110 < 0011 NO
1
0
0

## Slide 16: Figure 6–25 An 8-bit magnitude comparator using two 74HC85s.
Lowest-order comparator must have a LOW on A > B and A < B input and a HIGH on A = B input.

## Slide 17: Decoders
Binary decoder
4-bit decoder
BCD-to-decimal decoder
BCD-to-7-segement decoder
n inputs-to-2n outputs

## Slide 18: Decoders
Suppose we want to know when a binary 1001 occurs on the inputs of a digital circuit.
We can use a Decoder for this function.
Binary decoder
  The output is 1 only when:
    A0 = 1
    A2 = 0
    A3 = 0
    A4 = 1
This is only one of an infinite number of examples

## Slide 19
Determine the logic required to decode the binary number 1011 by producing a HIGH level on the output. LSB = A0 (right most)
A0 = 1, A1 = 1, A2 = 0, A3 = 1
X = A3A2A1A0

## Slide 20: Truth Table for 3-to-8 Line Decoder

## Slide 21: 3-to-8 Line Decoder

## Slide 22: 2-to-4 Line Decoder

## Slide 23: Decoders
4-bit decoder (4 line to 16 line decoder or 1 of 16 decoder)
Logic Diagram

## Slide 24: Decoders
4-bit decoder
  Binary inputs
Truth Table

## Slide 25: 3-to-8 Line Decoder using 2-to-4 Decoder

## Slide 26: 4-to-16 Line Decoder using 2-to-4 Decoder
A3
A2
A1
A0

## Slide 27: Decoders
BCD-to-decimal decoder
If 0011 is input, then output 3 is low and all other outputs are high Active Low output since bubbles on outputs.

## Slide 28: TASKS: Decoders
BCD-to-7-segement decoder

## Slide 29: Encoders
The process of converting from familiar symbols or numbers to a coded format is called encoding.
Decimal-to-BCD encoder
8-line-to-3-line encoder
“reverse” decoder function

## Slide 30: Encoders
Decimal-to-BCD encoder ( 10 inputs, 4 outputs)

## Slide 31: Logic Diagram of Decimal-to-BCD Encoder
A3 = 8 + 9
A2 = 4 + 5 + 6 + 7
A1 = 2 + 3 + 6 + 7
A0 = 1 + 3 + 5 + 7 + 9

## Slide 32: Code Converters
BCD-to-binary conversion
Binary-Gray conversions

## Slide 33: Example: BCD
BCD-to-Binary Conversion
One method of BCD-to-binary code conversion uses adder circuits. The basic conversion process is as follows:
1. The value, or weight, of each bit in the BCD number is represented by a binary number.
2. All of the binary representations of the weights of bits that are 1s in the BCD number are added.
3. The result of this addition is the binary equivalent of the BCD number.
A more concise statement of this operation is
The binary numbers representing the weights of the BCD bits are summed to produce the total binary number.

## Slide 34: Example: BCD
decimal number 87 can be expressed in BCD as
1000 0111
8 7
The left-most 4-bit group represents 80, and the right-most 4-bit group represents 7. That is, the left-most group has a weight of 10, and the right-most group has a weight of 1. Within each group, the binary weight of each bit is as follows:

## Slide 35: Example: BCD
If the binary representations for the weights of all the 1s in the BCD number are added, the result is the binary number that corresponds to the BCD number.

## Slide 36: Example: BCD
Convert the BCD numbers 00100111 (decimal 27) and 10011000 (decimal 98) to binary.
Write the binary representations of the weights of all 1s appearing in the numbers, and then add them together.

## Slide 37: Figure 6–43 Four-bit binary-to-Gray conversion logic.
Convert 1 1 0 0 to Gray
1
0
1
0
1
0
1
0
0
1
1
1

## Slide 38: Figure 6–44 Four-bit Gray-to-binary conversion logic.
Convert 1 0 1 0 to Gray
1
1
0
0
1
1
0
1
0
1
0
1
1

## Slide 39: Multiplexers (Data Selectors)
4-input multiplexer
Expanded multiplexers
Functionality:
Selection of a particular input
Route 1 of N inputs (A) to the output Y

## Slide 40: Multiplexers (Data Selectors)
4-input multiplexer
If Data-Select Inputs are 10, then Y = D2 If D2 = 0, then Y = 0. If D2 = 1, then Y = 1.

## Slide 41
What is the output Y if we have the following inputs?
0 1
1 0 1 0
1
1 1
1 0 1 0
0

## Slide 42: Figure 6–85. Like Problem 28.
If S0S1 = 11 and D3D2D1D0 = 1001, what is the output?
= 1

## Slide 43: Demultiplexers
Reverses the multiplexing function.
Sends the data input to the selected output.
Decoders can be demultiplexers.

## Slide 44: Demultiplexers
2-line-to-4-line demux

## Slide 45
Find the data-output waveforms for the demultiplexer.
S0 and S1 select which output line will receive the input data.
If data input is zero, then all outputs will be zero.

## Slide 46: Parity Generators/Checkers
Parity generator/checker
Sum of even number of 1s is always 0. Sum of odd number of 1s is always 1.

## Slide 47: Parity Generators/Checkers
Parity generator/checker
74HC280
even parity checker use even bits
even parity generator, the parity bit is taken at the sigma Odd output because this output is a 0