## Slide 1: Digital Fundamentals
CHAPTER 6 Functions of Combinational Logic

## Slide 2: Chapter Outline
6–1 Half and Full Adders
6–2 Parallel Binary Adders
6–3 Ripple Carry and Look-Ahead Carry Adders
6–4 Comparators
6–5 Decoders
6–6 Encoders
6–7 Code Converters
6–8 Multiplexers (Data Selectors)
6–9 Demultiplexers
6–10 Parity Generators/Checkers
6–11Troubleshooting Applied Logic

## Slide 3: Comparators
The basic function of a comparator is to compare the magnitudes of two binary quantities
In its simplest form, a comparator circuit determines whether two numbers are equal.

## Slide 4: Comparators
1-Bit Comparator
2-Bit Comparator
4-Bit Comparator

## Slide 5: Comparators
1-Bit Comparator - Exclusive NOR
The output is 1 when the inputs are equal

## Slide 6: Comparators
2-Bit Comparator
The output is 1 when A0 = B0 AND A1 = B1

## Slide 7: Example 6-5: Comparators
Apply each of the following sets of binary numbers to the comparator inputs in Figure 6–20, and determine the output by following the logic levels through the circuit.
(a) 10 and 10 (b) 11 and 10

## Slide 8: Inequality: Comparators
4-Bit Comparator
One of three outputs will be HIGH:
    A greater than B (A > B)
    A equal to B (A = B)
    A less than B (A < B)
To determine an inequality of binary numbers A and B, you first examine the highest-
order bit in each number. The following conditions are possible:
1. If A3 = 1 and B 3 = 0, number A is greater than number B.
2. If A3 = 0 and B 3 = 1, number A is less than number B.
3. If A3 = B 3 , then you must examine the next lower bit position for an inequality.

## Slide 9: Figure 6–23 What are the outputs for the given inputs?
A B 0110 > 0011 YES 0110 = 0011 NO 0110 < 0011 NO
1
0
0

## Slide 10: Figure 6–25 An 8-bit magnitude comparator using two 74HC85s.
Lowest-order comparator must have a LOW on A > B and A < B input and a HIGH on A = B input.

## Slide 11: Decoders
Binary decoder
4-bit decoder
BCD-to-decimal decoder
BCD-to-7-segement decoder

## Slide 12: Decoders
Suppose we want to know when a binary 1001 occurs on the inputs of a digital circuit.
We can use a Decoder for this function.
Binary decoder
  The output is 1 only when:
    A0 = 1
    A2 = 0
    A3 = 0
    A4 = 1
This is only one of an infinite number of examples

## Slide 13
Determine the logic required to decode the binary number 1011 by producing a HIGH level on the output. LSB = A0 (right most)
A0 = 1, A1 = 1, A2 = 0, A3 = 1
X = A3A2A1A0

## Slide 14: Decoders
4-bit decoder (4 line to 16 line decoder or 1 of 16 decoder)
Logic Diagram

## Slide 15: Decoders
4-bit decoder
  Binary inputs
  Active-low outputs (bubbles)
Truth Table
A3A2A1A0 Output 0 1 1 0 6 is low, all other outputs are high

## Slide 16: Decoders
BCD-to-decimal decoder
If 0011 is input, then output 3 is low and all other outputs are high Active Low output since bubbles on outputs.

## Slide 17: Decoders
BCD-to-7-segement decoder
Logic Diagram
Common-anode
Common Anode has all anodes of LEDs tied to +V

## Slide 18: Decoders
BCD-to-7-segment decoder
Truth Table

## Slide 19: Figure 6–35 Pin diagram and logic symbol for the 74LS47 BCD-to-7-segment decoder/driver.
Copyright ©2006 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
LT = Lamp Test - when LOW and BI/RBO is HI then all LEDs are ON BI = Blanking Input RBI = Ripple Blanking Input RBO = Ripple Blanking Output

## Slide 20: Figure 6–36 Examples of zero suppression using the 74LS47 BCD to 7-segment decoder/driver.
Tie RBI of Right to next left BI/RBO for leading zero suppression. Left most RBI is tied to ground.
Tie RBI of Left to next right BI/RBO for trailing zero suppression. Right most RBI is tied to ground.

## Slide 21: Encoders
Decimal-to-BCD encoder
8-line-to-3-line encoder

## Slide 22: Encoders
Decimal-to-BCD encoder ( 10 inputs, 4 outputs)

## Slide 23: Logic Diagram of Decimal-to-BCD Encoder
A3 = 8 + 9
A2 = 4 + 5 + 6 + 7
A1 = 2 + 3 + 6 + 7
A0 = 1 + 3 + 5 + 7 + 9
All odds

## Slide 24: Encoders
8-line-to-3-line encoder
If line 5 on input is high, then output will be 101. Assume only one input is high.

## Slide 25: Code Converters
BCD-to-binary conversion
Binary-Gray conversions

## Slide 26: BCD
Convert BCD number 00100111 to binary.
Could convert to decimal 27 and then convert to binary.
Can add weights.
80 40 20 10 8 4 2 1 0 0 1 0 0 1 1 1 1 1 10 2 100 4
10100 20
0011011 27

## Slide 27: Figure 6–43 Four-bit binary-to-Gray conversion logic.
Convert 1 1 0 0 to Gray
1
0
1
0
XOR

## Slide 28: Figure 6–44 Four-bit Gray-to-binary conversion logic.
Convert 1 0 1 0 to Gray
1
XOR
1
0
0

## Slide 29: Multiplexers (Data Selectors)
4-input multiplexer
Expanded multiplexers

## Slide 30: Multiplexers (Data Selectors)
4-input multiplexer
If Data-Select Inputs are 10, then Y = D2 If D2 = 0, then Y = 0. If D2 = 1, then Y = 1.

## Slide 31
What is the output Y if we have the following inputs?
0 1
1 0 1 0
1
1 1
1 0 1 0
0

## Slide 32: Demultiplexers
Reverses the multiplexing function.
Sends the data input to the selected output.
Decoders can be demultiplexers.

## Slide 33: Demultiplexers
2-line-to-4-line demux

## Slide 34
Find the data-output waveforms for the demultiplexer.
S0 and S1 select which output line will receive the input data.
If data input is zero, then all outputs will be zero.

## Slide 35: Parity Generators/Checkers
Parity generator/checker
Sum of even number of 1s is always 0. Sum of odd number of 1s is always 1.

## Slide 36: Figure 6–76. Problem 4. Find the sum based on the inputs. Note: We are adding A = 111 to B = 101.
0
0
1
1

## Slide 37: Figure 6–80 Problem 14. Plot the 3 outputs (A>B, A=B, A<B)
A3A2A1A0 B3B2B1B0 A>B A = B A<B 1 0 0 1 0 1 0 0 1 0 0 1 1 1 1 1 1 1 1 0 1 0 1 1 1 0 0 0 1 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 1 0 1 1 1 0 0 0 0 1
A>B
A=B
A<B

## Slide 38: Figure 6–84. Problem 22. Find sequence of digits that appear.
A3A2A1A0 0 0 0 0 0 1 0 0 1 9 1 1 1 1 undefined 0 1 1 1 7
3
2
1
0

## Slide 39: Figure 6–85. Like Problem 28.
If S0S1 = 11 and D3D2D1D0 = 1001, what is the output?
= 1